In the backdrop of a mercurial, ever-changing fashion world,Fariha knit tex Ltd considers its prime mission to suit every new taste, whim and demand of

Customers from around the world and all strains of human culture.

FNL acts on the basic premise that “fashion is an exploration into the images people seek to convey – about themselves and the way they live.”

So, in dealing with its target consumers, FNL mainly aims to know their perception about themselves and translates those into garments. Doing that, over the years, FNL designers have acquired an almost telepathic understanding of the consumers’ needs.

FNL has started manufacture and export garments since late 1990. Its mission is to produce the latest design; quality knit fabrics and apparels for international markets.

FNL is one of the few elite private sector business groups, which contributed wealth as well as welfare to the struggling economy of Bangladesh.

As time is essential to space so is taste to its products. The secret is love – which, paired with meticulous efficacy and a keen sensitivity to style, makes FNL an emerging brand destined to light up the horizon of fashion.

FNL has team of skilled and dedicated technocrats backed by adequate number of modern USA and European machinery and equipments to match international standard of all kinds of knitwear products.

General Information About The Factory:

Name of the factory:  FARIHA KNIT TEX LTD.Type : 100 % Export Oriented Composite knitwear Industry

Year of Establishment : 1997

Status ( Legal Structure ) : Private Limited Company

Annual Production capacity : 7000 ton of knit fabric ( Open & tubular form )

Total Manpower: Male- 3750 Female-1250

Address: Baroibogh,West Masdair , Fatullah,Narayanganj, Bangladesh.

DND ROAD

FNL

FARIHA KNIT TEX Limited is located at Baroibogh , in Narayanganj about 3 km from the BISIC

7Product mix:

- 100 % cotton

- CVC (Chief Value Cotton) (60/40)

- Grey melange

* 5 % Viscose & 95% Cotton

* 10 % Viscose & 90% Cotton

* 15 % Viscose & 85 % Cotton

- Ecro melange (2%)

- Camel melange (1%, 2%)

- PC (52/48)

Project Cost:   90 core Taka

Different Departments:

Production Oriented Department:

•	Yarn store

•	Raw fabric store & Raw fabric inspection section

• 	Knitting

•	Planning & Control

• 	Batching

•	Chemical store

•	Dyeing Section

•	Finishing Section

•	Dyeing lab section

•	Wet lab

•	Quality Control

• 	Maintenance

• 	Utility

•	Water treatment plant

Supporting department:

-	Prochrement

-	Merchandising

-	Marketing

-	IT

-	HRD

-	Finance & accounting

-	Medical

-	Personnel Administration

-	Security

REMARK:

It's a wonderful project. Though it's a new project but profitable for it's strong management The main draw back was there is no Effluent treatment But within some days The Effluent treatment plant will be completed.

FARIHA KNIT TEX Ltd.(Dyeing Department) Manpower List :

| No. | Section | Person |
| --- | --- | --- |
| 01 | GM/AGM | 01 |
| 02 | DM | 0l |
| 03 | ADM | 01 |
| 04 | SPO | 01 |
| 05 | P.O | 04 |
| 06 | Planning | 01 |
| 07 | Q.C / Q.I | 86 |
| 08 | Maintenance | 71 |
| 09 | Batch | 75 |
| 10 | Dyeing | 149 |
| 11 | Finishing | 139 |
| 12 | Store | 26 |
| 13 | Delivery | 29 |
| 14 | Washing | 23 |
| 15 | Accounts | 03 |
| 16 | Marketing | Ol |
| 17 | Store (Acc) | 02 |
| 18 | Ex.Of./'Time | 04 |
| 19 | Pion | 04 |
|  | Total | 621 |

Shift Change:

| Shift | From | To |
| --- | --- | --- |
| A | 8 A.M. | 8 P.M. |
| B _ | 8 P.M. | 8 A.M. |

Responsibility of production officer :

- Overall supervision of dyeing & finishing.

- Dyes & chemicals requisition issue & check.

- Program making, sample checking color measurement.

- Control the supervisors operators & helpers of machines .

- To give dye-line or the program slip according to daily production plan. Batch preparation   & pH check

- To rectify the finished fabric which rejected from quality control department .

- To check daily production report

- To study dye & chemicals nature delivery by the manufacture & applied them correctly to the production to get best product .

Job Description :

Title : Production Officer.

Dept.: Dyeing

Report to : Senior production officer

Job summery : To plan execute & follow up the production activities & control the quality production with related activities .

Title : Senior Production Officer

Dept.: Dyeing

Report to : Dyeing Manger

Job summery :To plan execute & follow up the production activities & control the quality production with related activities .

REMARK :

In this dyeing plan all the P.O ,S.P.O & D.M are technical person . Thus why efficiency of this section is very high .

List of Machines

| Department | Machine type | No. of machine |
| --- | --- | --- |
| Grey Fabric Store & inspection | Fabric inspection m/c | 3 |
| Batching | Back sewing m/c | 01 |
|  | Turning m/c | 02 |
|  | Plaiting m/c | 02 |
|  | Overlock m/c | 02 |
| Dyeing floor | Winch dyeing m/c (Environmental ) | 12 |
|  | Winch dyeing m/c (High Pressure) | 9 |
| Dark Room | Light Box | 02 |
| LAB | Ahiba Naunce-( Sample Dyeing m/c) | 04 |
|  | Fongs ( S-D.M ) | 02 |
|  | Lab Extractor | 02 |
|  | Dryer | 01 |
|  | Yarn Twist Tester | 01 |
|  | Incubator ( Oven ) | 01 |

| Lab | Verivide Light Cabinet Cac 120 | 01 |
| --- | --- | --- |
|  | Hot Plate (Single Burner) | 01 |
|  | Computer | 01 |
|  | Philips Hot Iron | 01 |
|  | Handy Data color | 02 |
|  | . Dryer | 02 |
|  | Rota Wash | 01 |
|  | Commercial Washer | 02 |
|  | Electronic Crock meter | 02 |
|  | Manual crock meter | 01 |
|  | Perspiration tester | 01 |
|  | pH Meter | 03 |

| Finishing | Dewatering & Detwisting m/c | 02 |
| --- | --- | --- |
|  | Efficient Shrinkage Dryer | 01 |
|  | Compactor(Tubular) | 02 |
|  | Santashrink Jumbo Dryer | 01 |
|  | Open width Compactor | 02 |
|  | Slitting & Dewatering m/c | 03 |
|  | Brushing m/c | 01 |
|  | Industrial Washer | 03 |
|  | Stenter | 01 |
|  | Calender | 01 |
|  | Backsewing m/c | 01 |
|  | Peach finish | 02 |

Lay out plan of FNL

Machine Specifications

Grey Inspection Machines :

1. Brand Name :UZU

Model : U2- 90031

Country Of Origin : Thailand

Serial No : 0095172

Motor: 210 HP

Power: 220 V

2. Brand Name: HSING CHENG

Model: HC-TIM -1500 mm

Country Of Origin : Thailand

No of motor: 02

Motor: 210 HP

Power : 220 V

Year of Manufacture : 2005

Batch Section:

1. Back sewing machine

Manufacture: MTG MECCANICA SNC

Country Of Origin : Italy

2. Turning Machines

Brand Name: HSING CHENG

Model: HC-TFM -1500 mm

Country Of Origin : Thailand

No of motor: 02

Motor: 210 HP

Power: 220 V

Year of Manufacture : 2005

3. Over lock Machine

Brand Name: JUKI

Model No: 3614

Country Of Origin : Japan

Lay out plan of Dyeing-Finishing floor

Dyeing Machines (Winch Dyeing Machine):

Machine No: 01

Brand Name: FONGS

Model: GN 6-SR -6T

Serial No :26012102

Country Of Origin : Honkong

Machine Type: ATM Machine

Capacity:  1000Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: O4

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Year Built : 2002

Machine No: 2

Brand Name: FONGS

Model: GN 6-SR -4T

Serial No :26012101

Country Of Origin : Honkong

Machine Type:ATM Machine

Capacity: 750 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 04

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Year Built : 2002

Machine No: 03

Brand Name: FONGS

Model : GN-18 M-4 T

Serial No :2G011473

Country Of Origin : Honkong

Machine Type :Environmental

Machine Capacity :600 Kg

Cycle time : 03 min

No of cycle	12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 04

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2001

Machine No: 04

Brand Name: FONGS

Model: GN-18 M-4 T

Serial No :24010297

Country Of Origin : Honkong

Machine Type :Environmental

Machine Capacity :500 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 04 No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2000

Machine No: 05

Brand Name: FONGS

Model: GN-6 SR-3T

Serial No :26012100

Country Of Origin : Honkong

Machine Type: ATM Machine

Capacity: 750 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed :250 m/min

No of Nozzle: 03

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required: 700 Kpa

Design temp. : 140 ° C

Year Built : 2002

Machine No: 06

Brand Name: FONGS

Model: GN-18 M-3T

Serial No :24010325

Country Of Origin : Hong kong

Machine Type :Environmental

Machine Capacity :1000 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle : 06

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2000

Machine No: 07

Brand Name: FONGS

Model: GN-6-2T

Serial No :23009446

Country Of Origin : Honkong

Machine Type :HTHP

Machine Capacity :250 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 02

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 1998

Machine No: 08

Brand Name: FONGS

Model: GN-18 M-2T

Serial No :23009199

Country Of Origin : Honkong

Machine Type :HTHP

Machine Capacity :500 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle : 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 1998

Machine No: 09

Brand Name: FONGS

Model: GN-18-2T

Serial No :23009200

Country Of Origin : Honkong

Machine Type: HTHP Machine

Capacity: 1000Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 06

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 1998

Machine No: 10

Brand Name: FONGS

Model: ECO-6-2T

Serial No :28015334

Country Of Origin : Honkong

Machine Type: HP/HT

Machine Capacity: 750 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 02

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built: 2003

Machine No: 11

Brand Name: AK

Model: GN-6-1T

Serial No :23009447

Country Of Origin : KOREAN

Machine Type :ATM

Machine Capacity :400 Kg

Cycle time: 03 min

No of cycle: 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required: 700 Kpa

Design temp. : 140 ° C

Year Built: 1998

Machine No: 12

Brand Name: AK

Model: GN-18 M-4 T

Serial No :26011472

Country Of Origin : Honkong

Machine Type :ATM

Machine Capacity :400 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 0 1

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required: 700 Kpa

Design temp.: 140 ° C

Year Built: 1998

Machine No: 13

Brand Name: FONGS

Model: ECO-38-6T

Serial No :28014582

Country Of Origin : Honkong

Machine Type: Environmental Machine

Capacity: 250Kg

Cycle time: 03 min

No of cycle: 12

Main pump speed :80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 02

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built: 2003

Machine No: 14

Brand Name: AK

Model: ECO-38-6T

Serial No :28014581

Country Of Origin : KOREAN

Machine Type: Environmental Machine

Capacity: 600 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 06

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2003

Machine No: 15

Brand Name: AK

Model: ECO-38-4T

Serial No :28015424

Country Of Origin : KOREAN

Machine Type: Environmental Machine

Capacity: 800Kg

Cycle time: 03 min

No of cycle: 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 02

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2003

Machine No: 16

Brand Name: FONGS

Model: ALLFIT -6O

Serial No : 26012103

Country Of Origin : Honkong

Machine Type :HP/HT Machine

Capacity: 100 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 02 N

o of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2001

Machine No: 11 B

Brand Name: FONGS

Model: ALLFIT -30

Serial No :29017180

Country Of Origin : Honkong

Machine Type :HP/HT

Machine Capacity :30 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 C 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required: 700 Kpa

Design temp. : 140 ° C

Year Built : 2004

Machine No: 11 C

Brand Name: FONGS

Model: ALLFIT -30

Serial No :29017183

Country Of Origin : Honkong

Machine Type :HP/HT

Machine Capacity :30 Kg Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2004

Machine No: 11 D

Brand Name: FONGS

Model: ALLFIT -30

Serial No :29017182

Country Of Origin : Honkong

Machine Type :HP/HT

Machine Capacity :30 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 0 1

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built: 2004

Machine No: 11 E

Brand Name: FONGS

Model: ALLFIT -30

Serial No :29017181

Country Of Origin : Honkong

Machine Type :HP/HT

Machine Capacity :30 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle : 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2004

Machine No: 12

Brand Name: FONGS

Model: GN-18

Serial No :24010324

Country Of Origin: CHINA

Machine Type :Environmental

Machine Capacity: 100 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed :80-150 m/min

Winch speed :250 m/min

No of Nozzle: 0 1

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2000

Machine No: 13

Sample Dyeing m/c:

Brand: Ugoloni

Origin : Italy

Capacity: 20 Kg.

Machine No: 14 A

Brand Name: FONGS

Model: ECO-38-1T

Serial No: 2801420

Country Of Origin : Honkong

Machine Type :Environmental Machine

Capacity: 150 Kg

Cycle time: 03 min

No of cycle: 12

Main pump speed: 80-150 m/min

Winch speed :250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2003

Machine No: 14 B

Brand Name: FONGS

Model: ECO-38-1T

Serial No: 2801421

Country Of Origin : Honkong

Machine Type :Environmental

Machine Capacity: 150 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required : 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2003

Machine No: 14 C

Brand Name: FONGS

Model: ECO-38-1T

Serial No: 28015419

Country Of Origin : Honkong

Machine Type :Environmental Machine

Capacity: 150 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed : 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 ° C

Year Built : 2003

Machine No: 14 D

Brand Name: FONGS

Model: ECO-38-1T

Serial No: 28015418

Country Of Origin : Honkong

Machine Type : Environmental

Machine Capacity: 150 Kg

Cycle time: 03 min

No of cycle : 12

Main pump speed: 80-150 m/min

Winch speed: 250 m/min

No of Nozzle: 01

No of motor: 08

Power: 415 V 3 @ 50 Hz

Water supply pressure req. : 300 Kpa

Compressed Air pressure required: 700 Kpa

Steam pressure required : 700 Kpa

Design temp. : 140 °C , Year Built : 2003

FINISHING MACHINES:

1. Slitting & Dewatering m/c

M/C quantity : 01

Brand-BIANCO

Origin-Italy

Pressure -4-4.5 bar

Output / Input Dancing R/1 pressure -0.5 bar

Power supply-400 volt

Utility Used : Electricity

Main Function :-To cut the tubular fabric for opening .

-To remove a slight amount of water in padding zone

2. Dewatering & Detwisting M/C

M/C quantity: 02

Brand -Santex

Origin-Switzerland

Extraction ( % )- 60 % ( approx }

Maxm Width capacity -140 cm

Workable Width -42 "

Year of manufacture: 1998

Other points :

Speed -66 yd/min ( Single jersey ) -50-55 yd/min (Rib/ Interlock )

Padder pressure -3.5 bar ( Single jersey ) -4-4.5 bar ( Rib / Interlock

There are shapes to control the dia of fabric.

4. SANTASHRINK JUMBO DRYER

M/C quantity : 01

Brand -SANTEX

Origin- Switzerland

Year of construction : 2003

5. Compactor (Tubular)

M/C quantity : 02

Brand -TUBETEX Origin-U.S.A

Year of construction :

Maxm line speed: 80 m/min

Useable line speed: 45 m/min

Maxm dia :55 "

Workable dia : 48 "

G.S.M Control : Maxm 20 % increase after compacting

M/c temp.- 95° C

Main Function : Dia Control, G.S.M Control, Shrinkage Control

Utility Used : Gas, Electricity, Steam

Sensor Position :

-Shoe pressure ( Two Shoe )

-Retard Roller ratio

-Pliater Ratio

-Edge drive ratio

-Near-far pressure

-Take-out roller ratio

-Conveyor Roller ratio

6. OPENWIDTH COMPACTOR:

M/C quantity : 02

Brand -TUBE-TEX

Origin-U.S.A

Maxm line speed: 60 m/min

Useable line speed: 30 m/min Maxm dia :95 "

Workable dia :90"

Steam box temp.-80° C

Feed R/L temp.-105° C

Over feed ( %)-upto 50 %

Shoe pressure : Maxm-18 Minm-5

Main Function :

-Width Control

-G.S.M Control

-To impart dimensional stability

Sensor Position :

-Shoe pressure ( One shoe )

-Retard Roller ratio

-Pliater Ratio

-Right-Left roller pressure

-Take-out roller ratio

-Conveyor Roller ratio

7. Compacting Calender :

M/C quantity : 01

Brand -SANTEX

Origin-Switzerland

Year of manufacture: 1998

8. STENTER :

M/C quantity : 02

Brand -TUBE-TEX

Origin-U.S.A

Maxm dia :111 "

Workable dia :100"

Temp.-120-140° C

Speed-20-50 m/min

Padder Pressure: 4-4.5 bar

Other points :

- Coarse & wales become align & even distribution by MAHLO in the feed side

- Bowing of fabric become straight

- 6 chamber ,12 burner ,12 blower.

- 12 nozzle at every chamber.

- 8 shape to control the width .

- Maxm width is not used because pin penetration is difficult & chains are

- Temperature control depends on shade condition . -In every chamber fabric width should be  same .

Sensor points : Fabric speed, Fabric width, Temperature, Over feeding speed.

Utility Used: Gas, Electricity, Steam

9.Sweading M/C :

M/C quantity : 01

Brand -TUBETEX

Model: 10 GS X 1952

Origin-U.S.A

Year of manufacture-2005

Voltage - 400 V

Normal Current - 96 amp.

No of Pile :03

No of Counter-Pile :03

Setting Point :

Taker -in- Tension (14 K/g)

Drum Tension (47 K/g)

Fabric Return Tension (15 K/g)

Plaiter Tension (14 K/g)

R.p.m of drum (22)

Fabric Speed (10 m/min)

Pile/Counter Pile Speed ( 80-90 m/min )

10.Raising M/C :

M/C quantity : 01

Brand -GEMATEX

Model: KRM 6725

Origin-Germany

Year of manufacture-1999

Voltage - 400 V

Nominal Current -63 A

No of Pile :12

No of Counter-Pile :12

Dyeing Lab Section :

Sample Dyeing M/C :

Brand Name: AHIBA NUANCE

Capacity : 20 pots

Pot Capacity: 150 ml

Country: USA

Purpose :Sample dyeing

Heating System : Infrared

Sample Dyeing M/C :

Brand Name: FONGS

Capacity : 12 pots

Pot Capacity: 150 ml .

Country :HONKONG

Purpose: Sample dyeing

Heating System : Electricity

Auto Dispensing M/C :

Brand Name :DATA COLOR

Capacity : 42 pots

Pot Capacity: 950 ml

Dispensing Capacity : 12 pots

Country: TAIWAN

Purpose : Laboratory dispensing & pipe ting

Software: USA

Max. Capacity :220 gm

Min.Capacity : 0.02 gm

Country: TAIWAN

Purpose : Laboratory dispensing & pipeting

Software: USA

Color matching Light Box:

Brand: Verivide

Light Source : 4 types TL 83,D65,F,UV

Country: UK

THE TYPES OF RAW MATERIAL(YARN STOCK) USED IN THE FNL AND THEIR SOURCES INCLUDING PRICES ARE GIVEN IN THE CHART OF DAILY YARN STOCK(AS NO:03/09/08)

Raw material is a unique substances in any production oriented textile industry It plays a vital role in case of continuous production & for high quality fabric .

Types of raw material:

•	Fabric

•	Dyestuff

•	Chemical & auxiliaries

Name & Sources of raw materials :

Grey Fabric :

•	Single Jersey

•	Single jersey with lycra

•	Interlock

• 	Terry

•	Single Lacoste

•	Double Lacoste

• 	Rib

•	Rib with Lycra

•	1 X 1 Rib

•	2X2 Rib

•	9X2 Rib

Fabric Sources :

• 	Knitexcel

•	Apple Knit

•	Energy group

•	Dream Fashion

•	Barnali Textile

•	Alahi knitting

•	Noor Textile

•	Mother Knitting

•	Microfibre

•	Ibrahim Knitex

Basic Chemicals :

•	Acetic Acid

•	Soda Ash

•	Caustic Soda

•	Oxalic Acid

•	Sodium hydrosulphate

Annual Requirment of Grey fabric :  4800 tons

Produced in KCL                              :  3000 tons

Brought in from other sources         :  1800 tons

Dyes :

The following dyes are used:

1.Reactive

2.Disperse

| Name of Dyes | Supplier | Store(kg) | Godown(kg) | Rate (Tk/Kg ) |
| --- | --- | --- | --- | --- |
| Cibacron Yellow - F4G | CIBA | 19.801 | 30 | 1690 |
| Cibacron Yellow FN2R | " | 60.811 | 300 | 1361 |
| Cibacron Orange – FNR | " | 12.444 | 0 | 2017 |
| Cibacron Scarlet -F3G | " | 6.374 | 0 | 2216 |
| Cibacron Red-FN3G | " | 67.485 | 270 | 2089 |
| Cibacron Red-FNR | " | 49.82 | 425 | 1194 |
| Cibacron Red-FN2BL | " | 16.666 | 380 | 1700 |
| Cibacron Scarlet -FN6G | " | 24.99 | 25 | 2153 |
| Cibacron Navy –WB | " | 80.956 | 300 | 435 |
| Cibacron Red -WB 150 % | " | 84.961 | 50 | 745 |
| Cibacron Red -HDN 200 % | " | 54.63 | 0 | 1400 |
| Cibacron Turquish –HGN | " | 57.081 | 225 | 702.5 |
| Bluton - BVB | " | 72.234 | 180 | 440 |
| Bezactive Yellow S-MAX | CHT | 62.355 | 875 | 742 |
| Bezactive Blue S-GLD | " | 8.423 | 0 | 1625 |
| Bezactive Blue SFR | " | 24.682 | 0 | 2048 |
| Bezactive Red S-3B | " | 26.714 | 75 | 705 |
| Bezactive Red S-MAX | " | 69.314 | 0 | 758 |
| Bezactive Yellow S-8G | " | 14.049 | 0 | 1203 |
| Terasil Black SRL-O1 | CIBA | 4.862 | 0 | 1200 |
| Terasil Black W-NS | " | 18.605 | 75 | 1789 |
| Terasil Blue BGE-01 | " | 34.241 | 25 | 1882 |
| Terasil Blue WBLS | " | 27.085 | 40 | 3000 |
| Terasil Navy GRLC | " | 18.443 | 0 | 967.94 |
| Terasil Red WRS | " | 36.855 | 100 | 2494 |
| Terasil Violet BL-01 | " | 17.049 | 25 | 2711 |
| Terasil Yellow W-4G | " | 23.571 | 15 | 930 |
| Remazol Blue-RR | " | 32.586 | 200 | 1073 |
| Remazol Yellow-RR | " | 22.713 | 100 | 962 |
| Remazol Red –RR | " | 9.573 | 475 | 962 |
| Remazol Brillient Yellow -3GL | " | 0.268 | 0 | 1800 |
| Remazol Tarquise Blue-G | " | 27.067 | 0 | 550 |
| Dychufix Yellow- EC | DYSIN | 134.14 | 200 | 452 |
| Dychufix Red -EC _ | " | 99.171 | 1660 | 494 |
| Dychufix Blue BR-XF 150 % | " | 24.208 | 60 | 1425 |
| Dychufix Red 2B-XF 150% | " | 45.414 | 140 | 475 |
| Dychufix Turquoise Blue –G | " | 66.083 | 0 | 427.5 |
| Dychufix Crimson MX-ED | " | 157.329 | 1360 | 591 |
| Dychufix Navy Blue EC | " | 185 | 1628 | 585 |
| Reactive Starfix Black –GR |  | 559.402 | 750 | 335 |
| Everzol Brill. Blue –RSPL |  | 42.561 | 50 | 1100 |
| Flabine -7GFE |  | 0.398 | 0 | 12000 |

Chemicals:

| Chemicals Name | Supplier | Price (Tk/Kg ) | Mode of Action |
| --- | --- | --- | --- |
| Kappasol AF 200 | Kappachem | 371 | Antifoam |
| Kappwet BOS | Kappachem | 350 | Wetting (Detergent) |
| Kappquest FE | Kappachem | 147 | Sequestering |
| Kappazone H53 | Kappachem | 142 | Peroxide stabilizer |
| Kappasoft BD | Kappaachem | 283 | Cationic Softener |
| Kappasoft SM | Kappachem | 284 | Silicon Softener |
| Kappatex R98 | Kappachem | 345 | Reducing Agent |
| Invatex PC | CIBA | 139 | Peroxide Killer |
| Silvatol FLN | CIBA | 467 | Anti Oil |
| Cibecel DBC | CIBA | 176 | Leveling gent |
| Irgasol CO-NEW | CIBA | 346 | Sequestering, |
| Cibapon R | CIBA | 324 | Soaping Agent |
| Eriopon OS | CIBA | 573 | Reducing agent |
| Invatex AC | CIBA | 180 | Core neutralizing |
| Cibafix ECO | CIBA | 396 | Fixing |
| Tinofix FRD | CIBA | 316 | Fixing |
| Irgasol DAM | CIBA | 271 | Fixing Remover |
| Cibatex AB45 | CIBA | 188 | High Temp. pH Stabilizer |
| Univadine DIF | CIBA | 468 | DisperseLevelingAgent |
| Romapon 173 | Dystar | 88.53 | Anticrease |
| RogIyr BIO97600 | Dystar | 517.84 | Engyme |
| Acetic Acid | Taiwan | 89 | Acid |
| Soda Ash | China | 26 | Alkali |
| Glaubar Salt | China | 16.28 | Electrolyte |
| Caustic Soda | China | 52.34 | Alkali |
| Hydrogen peroxide 50% | India | 45.4 | Bleaching Agent |
| Oxalic Acid |  | 75 | Acid |

Lay out plan of Lab Section

Tumble Dryer:

Model: G 511 V

Country: ITALY

Purpose : Drying

Mini Dryer:

Country: ITALY

Purpose : Drying

Temp.: Max 300°

Wash Fastness Tester :

Brand Name :Rota Wash

Capacity : 24 pots

Temp.: Max 100°

Country: UK

Lab Extractor M/C :

Country: UK

Purpose: Squeezing

Sequence of operation :

Lab dip approved

▼

Grey fabriC inspection

▼

Batching

▼

Scouring & Bleaching

▼

Enzyming ( If required )

▼

Dyeing

▼

Bath Drain

▼

Cold Wash

▼

Neutral With Acetic Acid

▼

Soaping

▼

Fixing (If required )

▼

Softening

Production Parameters :

| Process | Temp(▫C) | pH | Time min | M : L ratio |
| --- | --- | --- | --- | --- |
| Scouring - Bleaching | 98 | 11.5-12 | 60' | 1:8 |
| Enzyme Wash | 55 | 4.5-5 | 60' | 1:8 |
| Enzyme Deactivation | 70 |  | 10' |  |
| Reactive Dyeing (Light Shade) | 60 | 10.2-10.8 | 60' | 1:8 |
| Reactive Dyeing (Dark Shade) | 60 | 10.9-12 | 60' | 1:8 |
| White Shade | 98 | 10.5-11.5 | 20' | 1:8 |
| Turquish color dyeing | 80-90 | 10.9-12 | 90' | 1:8 |
| Polyester dyeing | 130 | 4-4.5 | 45' | 1:8 |

Grey Fabric Inspection :

In grey fabric inspection the available faults are

-Hole

-Loop

-Set up

-Needle breaking

-Needle mark

-Star

-Sinker Mark

-Yarn problem

-Patta

-Wheel mark

-Oil mark

-Oil spot

-Thin & Thickness

-Patty

-Group mark

Batching :

Batching preparation is the process where inspected grey fabrics are divided into different batches with reasonable quantity according to machine capacity, nozzle number in order to make them suitable for the further operation In batching. It must be carefully observed that each Nozzle of a machine contains equal length of fabric.

Sequence of Batching :

Grey fabric divided into batches

▼

Batches divided nozzle wise according to lengh & Dia

Instrument used :

-Turning m/c

-Plaiting m/c

-Weighting m/c

-Back sewing m/c

-Overlock m/c

Information checked:

-Order No

-Color

-Yarn Count

-Yarn lot

-Yarn brand

-Knitting factory

-Machine No

-Roll No]

Pre-treatment:

-For scouring & bleaching at first the fabric is loaded on to the bath .

-Required amount of water is taken to the bath .

-Wetting Agent & Anti creasing Agent is added.

-Scouring Agents (Caustic/Soda) & Stabilizer are added by the aid of dosing when the temperature reaches at 50° C.

-H202 is added by the aid of dosing system for 5' .

-Temperature is raised to 98° C & the process is carried for 6O'

-The liquor are drained at 80° C.

-After that chemical wash & enzyme wash are done.

Curves for Pre-treatment:

Scouring & Bleaching:

Chemical Wash:

Enzyme Wash:

Dyeing Light /Medium Shade:

Dyeing Bath Preparation :

- Auxiliaries are added at 50° C

-Salt added by dosing system ( time : 10-20')

- pH maintained at 6.5-7

-Color dosing at 6O° C for 20'

Exhaustion & Fixation :

-After 30' soda ash added by dosing for 30-35'

-pH checked & maintained at 10.5

-Dye bath is kept at 60° C for 40-60'

-After every 10' the sample is checked fixation occurs during this time.

-Rinse for 10' & the bath is drained.

Neutralization :

-The material should be neutralized to remove alkaline condition at room temperature by acid wash for 15 min & rinsing will be carried on for 10 min.

Soaping :

-Then soaping agent is added & temperture raised to 90°-100°C for 10 min.

-The bath is cooled 7 rinsed for 10 min.

-Dye bath temperature then cooled to 60° C.

Softening:

Softener is applied to soften the fabric as well as it improves the hand feel. The material is treated at 60°C for 20 mins. Then rinsing again & material unload.

Procedure of Dark shade :

At first the bath is set at 50° C & take the right volume of water in the dye bath.

▼

Required amount of wetting agent is added.

▼

Caustic soda is added & second heat command 60°C & stabilizer is added also.

▼

H202 is dosed & 10' runs.

▼

Temperture  raised to 100° C & run the material for 30'

▼

Cooling the bath at 75°C & bath is drained .

At 90° C the material is run for 15 mins

▼

Cooling the bath to 75°C to darin

▼

Add Acetic Acid to neutralize the whole bath of fabric & run time is 20'

▼

Rinse the fabric for 5' & bath is drained .

▼

New water from reserver is taken & pH should be 4.5-5 .

▼

Enzyme is injected to the bath . Run time is 60' at 55°C

▼

Temp. raised to 70° C & run time 10' & then drain

▼

Again new water is taken & dosing of glaubar salt for 20' & pH should be check

(pH =7)

▼

Color dosing for 30' at 50°C

▼

Soda is added by dosing for 40'at 50°C

▼

Then raise the temp. & run the fabric for 35-60'.At this time after every 10' the sample is checked.

▼

Rinse the material for 10' & bath is drained.

▼

At room temp. acid treatment is done for 20'& rinse the material for 5'

▼

Soaping is done at 90°C for 10 min & bath is drained.

▼

Fixing agent is added at 50° C & run time is 20' & bath is drained

▼

Softening is done at 60° C for 20'& balli is drained.

▼

Finally the fabric is unloaded.

White Shade:

At first Scouring bleaching chemicals are added to the bath & they are treated at 98°C for 60'

▼

Temp. is lowered at 80°C & OBA is added.Run time is 10'.

▼

Temp. is raised to 98° C & Run time is 20'.

▼

Then enzyme treatment is applied & then softening occurs

Dyeing Curve:

Normal Hot:

Chemical Hot:

Fixing & Softening (if dark shade):

Softening:

Stripping Recipe:

-First of all these two chemicals are taken & treated with fabric in cold temperature for 30 min.

Soda ash =0.5 g/L

Bleaching powder =0.5 g/L

Then Direct drain is done.

-After that some other chemicals named below are treated at 98°C for 45 min.

Anticreasing Agent =0.3 g/L

Levelling Agent =0.3 g/L

Wetting Agent =0.3 g/L

Caustic soda =1-2 g/L

-After that 3-5 g/L Reducing Agent is taken and treated at 80°C for 10'.

Then Direct Drain is done.

-After that half or full scouring takes place

-Lastly fabric is treated by acetic acid.

Stripping for white :

-First of all these two chemicals are taken & treated with fabric in cold temperature for 30 min.

Soda ash =0.5 g/L

Bleaching powder =0.5 g/L

Then Direct drain is done.

-After that these two chemicals are taken & treated with fabric at 98°C for 60 min.

Hydrose =1-2 g/L

Caustic Soda =1-2 g/L

-Lastly fabric is treated by acetic acid.

Machine Wash:

Add hydrose (6 g/L) & caustic Soda (6 g/L)

▼

Run 20' at 110° C

▼

Run 10' at 95° C

▼

Run 10' at 80° C

▼

Run 10' at 60° C

▼

Run 10' at 40° C

▼

Drain

FINISHING

Textile finishing, in a restricted sense, is the term used for a series of processes to which all bleached, dyed, printed & certain grey fabrics are subjected before they are put to market.

OBJECTIVE OF FINISHING:

-Improving the appearance,luster, whiteness etc.

-Improving the feel, which depends on the handle of the material & its softness, suppleness, fullness etc.

-Wearing qualities, non- soiling, anticrease, antishrink comfort etc .

-Special properties required for particular uses -water -proofing flame proofing etc .

-Covering of the faults in the original cloth .

-Increasing the weight of the cloth .

FINISHING EFFECTS:

-Easy care .

-Crease recovery.

-Dimensional stability

-Good abrasion resistance

-Improved tear strength

-Good sew ability

- Soft or stiff handle

-Shine or luster

SEQUENCE OF OPERATION:

For Open fabric:

Slitting

▼

Stenter( Softener used )

▼

Compactor

For tubular fabric:

Padder  (Softener used)

▼

Drying

▼

Compactor

FINAL INSPECTION REPORT:

For final inspection , Inspection table & Inspection m/c is used .

The 4-point system is given below-

| Size of Defect | Penalty point |
| --- | --- |
| Less than 3 inches | 1 |
| 3-6 inches | 2 |
| More than 6- 9 inch | 3 |
| More than 9 inch | 4 |

Size of holes & opennings-

| 1 inch or less | 2 |
| --- | --- |
| More than 1 inch | 4 |

Some general rules of the inspection are-

- Not 1 metre of cloth is penalized more than 4 points.

- Cloth is inspected on face side only unless specified.

- If the total defect parts per 100 yards of fabric are 40 or more the fabric will be rejected.But it may be changed according to buyer’s requerments.

REMARK:

FNL strictly follow up the production parameters like Temp, M:L ratio pH check etc. As they do some difficult shade it takes more time for the production of the Batch.The production officer & Sr. production Officer try their best to reduce the production time.

SELF SHADE COLLECTION

| Recipe | Sample |
| --- | --- |
| DY.B.B=2% GLUBER SALT=32g/l SODA=10g/l |  |
| DY.B.B=1% GLUBER SALT=30g/l SODA=10g/l |  |
| RE:NAVY RGB=1% GLUBER SALT=32% SALT=10% |  |
| RE:NAVY RGB=2% GLUBER SALT=44% SALT=14g/l |  |

| Recipe | Sample |
| --- | --- |
| DY.YRXF=2% GLUBER SALT=44% SODA=14g/l |  |
| DY.YRXF=1% GLUBER SALT=32% SODA=10g/l |  |
| DY:R3BXF=1% GLUBER SALT=32% SODA=10g/l |  |
| DY:R3BXF=1% GLUBER SALT=44% SODA=14g/l |  |

SAMPLE COLLECTION

| Recipe | Sample |
| --- | --- |
| DY.Y.3RXF=.62% DY.R.3BXF=.24% RE.B/GWF=6.6% COMMON SALT=100g/l SODA=30g/l |  |
| AS.Y-4GL=.96% RE.TGB=.O3% RE.N.RGB=.042% GLUBER SALT=32g/l SODA=10g/l |  |
| DY-YELLOW-4GL=1.32% REMO-T.BLUEG=.83% REMO-NAVY-RGB=,25% GLUBER SALT=32g/l SODA=10g/l |  |
| BMB=.06% B.TEX=.18% |  |

QUALITY ASSURANCE SYSTEM

The quality assurance department is assigned to maintain consistently uniform quality of the material in process & various stages of its manufacturing.

Objects of quality control

1.Research

2.Selection of raw material

3.process control

4.Process development

5.Product testing

6.Specification test

Scope of quality control, quality assurance & testing :

-Testing lab

-Machine auditing system

-A good training system

-Excellent analytical

-Technical Expe rtise

In KCL following flow diagram is followed-

Yarn Processing

▼

Yarn test

▼

Pass		                           Fail

▼                                                     ▼

Knitting                                   Send to spinning mill

▼

Grey fabric inspection

Pass                                                   Fail

▼                                                     ▼

Grey store                                    Send to store as reject

▼

Batch making

▼

Dyeing

▼

Dewatwering

▼

Drying/Stenter

▼

Compacting

▼

Fabric checking

▼

Lab                Inspection                Shade

▼

Pass                                                    Fail

▼                                                      ▼

Delivery

▼                          Raecuable                                             Reject

Send to concern                                                                              ▼

Depertment                                                                   Send to store as reject

I.aboratory :

Lab is the heart of the textile industry Higher precision lab can aid easily to achieve the goal of the organization Before bulk production a sample for the approval from industry is sent to the buyer As per the requirement of the buyer the shade is prepared in a lab considering the economical aspects .

LABORATORY STANDARD DYEING CURVE :

Salt Alkali & acid requirement:

| Dyestuff | % | <0.5 | 0.6 -1.0 | 1.10-2.0 | 2.10-3.0 | 3.10-5.0 |
| --- | --- | --- | --- | --- | --- | --- |
| Gluber Salt | g /L | 20 | 30 | 40 | 50 | 60 |
| Soda ash | g /L | 10 | 10 | 15 | 15 | 20 |
| Acetic Acid | ml | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |

Amount of Caustic :

| Dye | Shade % | Amount(g/L) |
| --- | --- | --- |
| Black | 6-7 | 1 |
| Red | >5 | 0.5-1 |

For Disperse Dye :

| Chemicals | Limit (g/L) |
| --- | --- |
| UNIVADINE DIF | 1 |
| CIVATEX -AB- 45 | 1 |
| Acetic Acid | 1 |
| pH | 4-4.5 |
| Time | 45 min |
| Temp. | 130▫C |

For Reduction Cleaning

| Chemicals | % | Medium Shade | Dark Shade |
| --- | --- | --- | --- |
| Detergent | g/L | 0.5 | 0.5 |
| Caustic Soda | g/L | 1 | 2 |
| Hydrose | g/L | 2 | 4 |
| Acetic Acid | g/L | 0.5 | 0.5 |

Lab line:

1.Standard sample :

The buyer to the merchandising section of the industry gives the order by colored swatch or by using PANTONE BOOK CODE. This is called Standard sample. The sample is measured by the CCM to get the recipe. The most recipe is chosen by metamarism value under three light source, price & dyestuff availability. Naturally up to 0.5 is accepted Sometimes some buyer supply the reflectance curve & reflectance % of different wavelength from 400 -700 nm. Data are input to the computer, most recipe is chosen by same way .

2. Lab trial :

Getting the recipe the lab officer produce lab trial & match with standard according to buyer requirement Lab trial is made by the AHIBA dyeing machine.

| PROGRAM NO | TEMPERATURE (▫C ) | TIME (min) |
| --- | --- | --- |
| 01 | 100 | 60 |
| 02 | 90 | 60 |
| 03 | 80 | 60 |
| 04 | 60 | 60 |
| 05 | 130 | 45 |
| 06 | 98 | 45 |

Physical test of fabric :

-Fabric weight

-Dimensional Changes in lengthwise

-Dimensional Changes in widthwise

-Seam Slippage

-Spirility test

-Pilling Resistance

-Softness test

-Hairiness test

Chemical test of fabric :

- Fastness to rubbing

- Fastness to washing

- Fastness to perspiration

Besides these, for the best qualified production these Chemical Test should be performed-

-Fastness to light

-Fastness to heat

-Fastness to sea water

-Fastness to chlorinated water

-Fastness to actual laundering

Finished fabric Inspection :

The final product should pass against the norms given by the buyer. The following tests are done-

-Shade check

-Gsm test

-Width or diameter test

-Shrinkage test

-Crocking test

-Pilling resistance test

-Color fastness to test

-Color fastness to perspiration

-Dimensional stability

Shade check :

The shade achieved is to be checked several times while in process & at finished state to ensure the customers demand under recommended light source .Generally the shade is checked at the following stage

-After dyeing

-After drying

-After trial for finishing

-After finishing

During dyeing period in QC there is a shade matching sequence:

Scoured sample

▼

Engyme sample

▼

Salt Sample

▼

Soda sample (after 10 min)

▼

BD sample ( 60▫C × 20 min)

▼

Normal hot sample

▼

Acetic acid sample

▼

Chemical hot sample

▼

ECO sample

▼

Softener sample

For this the following equipments are used :

1.Verivide light box

Manufacturer: Cundy building , frog island Origin : England

Light Source :

D-65 ( artificial day light )

TL-84 ( Shop light )

F ( florescent light )

UV ( Ultraviolet Blue light )

Procedure of GSM measurement by GSM cutter :

1. Cut the fabric with the G.S.M cutter.

2. Weight the fabric with the electric balance .

3. The cut sample is 100 sq.cm. The weight of the cut sample is multiplied by 100.

4. The result is the G.S.M of that particular fabric .

Suppose ,

The weight of the fabric is 2.51 gm. That means the G.S.M of the fabric is 251 gm.

Specification of GSM cutter :

Name: G.S.M CUTTER

Manufacturer: James H.Heal & Company limited.

Origin : England

Width or diameter test :

After finishing the fabric diameter or width is measured by a measuring tape. If the width is more or less compactor is used to set the required width If width is more ,then lengthwise tension is increased And if width is less it is increased by shape .

Shrinkage test :

The shrinkage properties is one of the most important properties to be checked for the knitted fabric .

For this the equipment used :

Name: Electrolux Washcator

Manufacturer: James H.Heal & Company limited.

Origin : England

There is a water label in m/c . Automatically water entered up to this label Then detergent

( 10 gm ) is added for per garment The useable program for Washcator are

| Temperature (▫C ) | Time (min) |
| --- | --- |
| 40 | 60 |
| 45 | 64 |
| 50 | 81 |

The washing methods:

Based on ISO 6330 ,3759 , 5077 .

Rubbing fastness test :

Rubbing fastness is tested by crock meter .

Name : Electronic Crock meter

Manufacturer: James H.Heal & Company limited. Origin : England

Test method : ISO 105 x 12. Dry & Wet rub is including in this method.

Pilling Resistance Test :

Name : ICI Pilling Test

Manufacturer: James H.Heal & Company Ltd.

Origin : England

Test method : EN ISO 12945-2

Description :

For wool / wool Blends / Elasthane Blends

-7200 revolutions

-1 revolution / sec

For other type of fabric

-14400 revolution

-1 revolution / sec

Color Fastness to Wash:

"Color Fastness " is the resistance of the color to fade or bleed by washing ,light ,water dry-cleaning chlorine perspiration & ironing .

Test method : ISO 6330,3759,5077.

Equipment Used:

1.Rota Wash

M:L = 1:50

Multifilament Size = 10*4 cm

Sample Size =	10*4 cm

Temp.	= 50°C

Time	= 30 min

Chemical Used : Detergent ECE (4 g/1 ),Na-per borate ( 1 g/1 )

Shade change is measured by color change scale & staining scale.

2.Washcator Washing m/c

Color Fastness to perspiration :

Test Method : ISO -105 E04

Temp = 37 +2°C

Time : 4 hr

Dry Temp = 60° C

M:L = 1: 50

Wet Time: 30 min

Multifilament Size = 10*4 cm

Sample Size =	10*4 cm

pH :8-5.5

| Chemical Used: | Alkali (gll) | Acid ( g/1) |
| --- | --- | --- |
| 1-histadine mono hydrochloride | 0.5 | 0.5 |
| Sodium Chloride | 5 | 5 |
| Di-sodium Hydrogen Orthophosphate | 2.5 | 2.2 |
| Ph | 8 | 5.8 |
| Distilled water | 1000 ml | 1000 ml |

Dimensional Stability:

This is checked by spirility test . Equipment Used :

Quick wash m/c

Template Size :

- 38 "x 38"

- 25" x 25"

Temp.= 50° C

Time = 12 ' (Wash & Dry)

REMARK :

In this modern world the buyer requirement is increasing day by day. And they are conscious about Quality of product more To fulfil this QC department has a lot to do Online. QC also check the following fault- Hole, Fly yarn, Dye stain, Chemical Stain, Uneven shade , Meter to meter Variation, compactor Crease, Patchy dyeing, Yam contamination, Sinker mark, dyeing Crease etc.

So QC department is very much important in dyeing section .

Maintenance :

Maintenance is a process by which equipment is look after in such a way that trouble free, Service & increased machine life can be ensured & specific product quality required by customers is sustained.

On time maintenance increase m/c lifetime & ensures trouble tree services.

MAINTENANCE OF MACHINERY

Preventive maintenance:

Preventive maintenance is a predetermined routine actively to ensure on time inspection/checking of facilities to uncover conditions that may lead to production break downs or harmful dcscription.

Break down maintenance:

In this case repairs are made after the equipment is out of order & it can not perform its normal functions.

Routine maintenance:

Maintenance of different machines are prepared by expert engineer of maintenance department. Normally in case of dyeing machine Maintenance after 30 days complete checking of different important parts are done.

MANPOWER  SET UP FOR MAINTENANCE:

| Position | No of person | Department. |
| --- | --- | --- |
| B.SC Engr. | 2 | Elect. & Mechanical Elect .& Mechanical |
| foreman | 2 | Elect. & Mechanical |
| Filter | 2 | Elect. & Mechanical |
| Assistant Filter | 2 | Elect. & Mechanical |
| Welder _ | 2 | Elect. & Mechanical |
| Helper | 6 | Elect. & Mechanical |

MAINTENANCE PROCEDURE:

Normally preventive maintenance is done here. For wlnch dyeing m/c it is kept for 15 days & for finishing floor it is kept for I5 days. During maintenance procedure following points should be checked.

CHECK LIST FOR DIFFERENT  PARTS

Maintenance : Mechanical

| SL NO. | Items needs to be checked & serviced |
| --- | --- |
| 1 | Grease the m/c bearing |
| 2 | Cleaning of drain valves, replace sesls if required |
| 3 | Check air supply filters, regulators auto drain seals g fd I I d |
| 4 | Clean filters element & below out |
| 5 | Greasing of unloading roller bearing |
| 6 | Checking of oil levels & bolts of unloading roller gearbox |
| 7 | Complete cleaning & machine |
| 8 | Checking unloading roller coupling & Packing |
| 9 | Checking & cleaning (if required) of main vessel level indicator |
| 10 | Check the oil level pump bearing & refill if required |
| 11 | Check the function or heart & cool modulating valves |
| 12 | Check all belts & belt tension |
| 13 | Check all door seals |

Maintenance	: Electrical

| SL NO. | Items needs to be checked & serviced |
| --- | --- |
| 1 | Check main panels |
| 2 | Check panel cooling fan & clean its filter |
| 3 | Clean main pump inverter & its cooling fan |
| 4 | Check all circuit breaker ,magnetic ccnductors & relays |
| 5 | Check current setting of all circuit breaker & motor over load |
| 6 | Visual checking of all power & ccntrol cables |
| 7 | Check aII motor’s terminals |
| 8 | Check & clean fluff & dirt at all motor fan covers |
| 9 | Check DC drive of neel motors |
| 10 | Check all pressure switches |
| 11 | Check calibration of main vessel & all addition tank |
| 12 | Check all signal isolators |
| 13 | Check setting & operation of lid safely switches |
| 14 | Check setting of tangle sensors |
| 15 | Check all pneumatic solenoids |
| 16 | Check all indicating lamps |
| 17 | Check calibration of heating/ cooling modulating valve |
| 18 | Check all on/off switches |

MAINTENANCE TOOLS & EQUIPMENTS:

The most important maintenance tools that are used frequently are tabulated.

| Maintenance tools | Function |
| --- | --- |
| Tread trap | Joining of broken metallic parts |
| Cutting disc | For cutting pipes, rods |
| Globe valve | Fitting for steam line |
| Union | Fitting for water, steam line |
| Union Elbow | Fitting for water, steam line |
| Gear oil | Lubrication |
| Cutting oil | Lubrication |
| Hydraulic oil | Lubrication |
| Oil gun | Oil application |
| Spanner | Tightening of nut bolts |
| Master range | Tightening of nut bolts |
| Flat/Star screw driver | Screw tightening & loosening |
| Hacksaw blade | Cutting |
| Spray gun WP40 | Spraying a chemical named WP40 |
| Drill m/c | Drilling to make hole |
| Grinding m/c | Grinding |
| Hacksaw Frame | Cutting |
| Grease | Lubrication |

REMARKS:

Maintenance of M/C's are very essential to prolong the m/c life and good maintenance is important consideration. ln this industry maintenance program is done by expert maintenance team So very few times production are due to m/c problem. In FNL there is ON-LINE reporting for maintenance so rest result can be obtained in shortest time.

AVAILABLE FACILITY OF UTILITY

| UTILITY | Source |
| --- | --- |
| Electricity | PDB & Generator |
| Gas | TITAS |
| Compressed air | Compressor |
| Steam | Boiler |
| Water | Natural Water by pump |
| Temp.Control | AC chiller |
| ETP | Drain out water |

STEAM:

Equipment used : Boiler

No of boiler - 03

Type of boiler : Horizontal, Fire tube boiler

Brand :LOOSE INTERNATIONAL (Germany)

CLAVER BROOKS(U.S.A)

Capacity  - 10 ton/hr (Loose International)

- 8 ton/hr( Claver brooks )

Fuel	    - natural gas,Diesel.

Steam Consumption : 2300 kg/hr for 1200-1500 products.

Steam pressure : 7-8 bar

Water pressure : 3-4 bar

Steam temp: 180°-190°C

Boiler Temp: 300°C

Chemical Used: NaCI Solution, NALCO 450 ( Scale Remover)

COMPRESSED AIR:

Source : Natural Air

M/C Name: Compressor

Brand: BOGGE (Germany)

CECATTO (ITALY)

No of m/c : 04

Capacity : 27,0001/hr, 1800 1/hr.

Unloading pressure :7.2 bar

Loading pressure : 5.6 bar

Chemical Used: Grease, Oil AMERILUBE

ELECTRICITY:

Source :PDB & Generator.

Equipment used: gas generator

Manufacturer: Wartsila-Frank

No of generator: 02

Gas engine used. 12 cyl. Per engine

Overall efficiency: 80%

Heat recovery : from 4 engines.

Cylinder capacity: 2.2 MW

Ignition pressure: 90 bar

Piston speed : 9 m/sec

Pressure of gas : 60-62 milibar

Air pressure: 7 bar

Electricity take up from PDB: 1.5 mw/sec

Mixture of gas air ; 1:18

Capacity: 1 MW

GAS :

Gas is mainly used for steam production. The gas is used from TITAS

Generally 2500 CFT gas is required to produce 1 ton steam/hr.

WATER:

| Pump | No of pump | Capacity |
| --- | --- | --- |
| Submersible | 05 | 100-125 m3 /hr |
| Booster | 14 | 100-125 m3 /hr |
| Centrifugal | 10 | 100-125 m3 /hr |

Technical Details :

Water : Water Is supplied by pump.Pump supplies water on the basis of pressure .Pump pressure ranges from 0-10 bar. Water is stored in water treatment plant. The water is collected from the 120 ft below to the earth .In water softening plant this water is treated with resins mainly.

IN KCL there are three water treatment vessels. Capacity of these are :

1- 50,000 l/hr

2- 100,000l/hr

3- 250,000l/hr

Sequence of water treatment plant-

-	Iron Remover

-	MGF/ ACF ( TDS Remover)

-	Softener

COMPRESSOR

Natural gas is drawn by pipe through the filter above the compressor & the air is compressed. In such a case the air becomes slightly hot. Hence cold water is drawn to reduce the temperature of compressed air. Thus the cold water becomes slightly hot & goes through outlet pipe to the overhead reservoir. Then the water falls slowly through a compressed air along with some vapors are transferred to the reservoir where the vapours are condensed & outlets drop by drop.

The moist compressed air is transferred to the dryer& a slight warm compressed air is delivered to require sections of KCL.

Steam:

Steam is an important utility for dyeing section. Steam produced by the boiler Supply water is simply treated in the boiler section by the two softener tank Then water reserves to the feed water tank & this feed water tank warms the water Then water passes to the boiler which produces steam & that steam supplies to the factory .

Main parts of the boiler :

-Gas Chamber

-Blower

-Gauge glass

-Safety valve

-Burner

Electricity :

It is impossible to continue the production without electricity. A frequent supply of electricity is necessary for soundless production. In KCL all machines in dyeing & finishing sections are provided electricity by the own generator of the industry .

UTILITY CONSUMPTION:

Water-80 l/kg of material

Gas required - 40 m3/hr

Electricity - 950 Kw/hr

COST OF DIFFERENT UTILITIES:

I unit electricity - 2.60 Tk

1 Kg Steam- 0.50 Tk

1 Ton Water - 7.30 Tk

Remarks :

For smooth running of a factory utilities are unavoidable. It has no direct use but help in the production So, utility should have the proper characteristics to met up the production parameter.

FREQUENCY OF INVENTORY UPDATE:

• Monthly inventory control

• Annual inventory control

SCOPE OF INVENTORY CONTROL:

- Raw materials

• Dyes store

• Other chemicals

• Grey fabrics

- Finished fabric

- Spare parts

- General store:

• Capital equipments

• Accessories

• Stationary

• Maintenance parts

INVENTORY SYSTEM FOR RAW MATERIALS:

• Raw materials partially received from production planning & directly from Head office.

• Material receiving & inspection report (MRIR) is prepared. Received quantity is mentioned & noted down.

• Submitted to QC dept. Some are OK & few are rejected.

• Entry of data of goods in DATATEX.

• Goods are arranged according to OK or rejected group.  Department gives store requisitionto warehouse.

• As per requisition materials supplied & this record are noted down.

STAGES OF GREY FABRIC INVENTORY CONTROL:

• After knitting production

• Grey inspection

• Warehouse

• Batch preparation  Dye house

STAGES OF FINISHED FABRIC INVENTORY CONTROL:

• Finishing section

• After final inspection

• Warehouse

| STORE CAPACITY: |  |
| --- | --- |
| * Dyes & chemicals | : 100 tons |
| * Grey fabrics | : 50 tons |
| * Yarn store | : 100 tons |
| * Set range of dyes/chem. | : 4-5 t/day |

REMARK:

- The inventory system of KCL covers both knitting & dyeing inventories.

- The space is noticed to be insufficient considerably.

Knitting Rate / Kg

| S/j | 9 (TK/K g) |
| --- | --- |
| S/j Lycra | 35-40 " |
| 1X1 Rib | 11-14 " |
| 2X2 Rib | 22-25 " |
| 9X2 Rib | 28-30 " |
| Lacoste | 16-18 " |
| Interlock | 18-20 " |
| Flat Knit _ _ | 200 " |
| Engg. Stripe (a)S/j (b)S/j Lycra | 100-120 " 150-160 " |

Yarn Costing /Kg (L.C Value)

| 26 s | 2.55-2.60 Dolles |
| --- | --- |
| 28 s | 2.60-2.65 " |
| 30 s | 2.65-2.70 " |
| 34 s | 2.85-2.87 " |

Melange (Local)

| 26 s | 3.65-3.70 Dolles |
| --- | --- |
| 28 s | 3.50-3.65 " |

Chemical Costing /Kg

| Light Color | 25 Tk |
| --- | --- |
| Deep Color | 35 " |
| Black | 40 " |

Dyestuff Costing /Kg

| Light Shade | 20 Tk |
| --- | --- |
| Deep Shade | 30 " |
| Black Shade | 40-45 " |

Special Treatment

| Enzyme Wash | 10 Tk/Kg |
| --- | --- |
| Silicon Wash | 10 " |
| Super Soft | 10 " |

Finishing Section :

| Padder | 5 Tk/Kg |
| --- | --- |
| Dryer | 10 " |
| Compacting (Tubular) | 10 " |
| Compacting (Open) | 25 " |
| Stenter | 25 " |
| Slitting | 5 " |
| Sweading | 30 " |

REMARKS:

FNL does not provide us all the documents of costing, because it is confidential.So this Chapter is not so sufficient to analyze the costing of product.

FNL is 100 % export oriented industry. All the goods produced in this industry are exported into various foreign countries . Name of the main buyers of this mill are given below :

• H&M

• OKAIIDI

• CAMAIEU

• CARREFOUR

• JULES

• DECATHLON

• SPRIT

• QUICK SILVER

• BIZBEE

• KNIT LINE

• S.OLIVER

• AMS INTERNATIONAL

• RIPCURL

• BETTER BARCLAY

IMPORTING COUNTRIES :

Following countries mainly imports products from FNL through many internationally well recognized buyers .

•	Europe Countries like UK France Germany etc

•   U.S.A

MANPOWER:

Marketing plays a vital role in the field of displaying/showing the good criteria of the products to the buyer & to communicate with the buyer .there about 30 people in the marketing section of the industry .

Marketing Strategy :

Marketing strategy is a very important factors to sale the products to the buyers If the marketing strategy Is not so developed it will be very hard to reach the goal In case of garments marketing the dealings with the buyer is a very important factor.

In one composite mills Ltd. Mainly senior marketing officers ,merchandisers & higher officials deal with the buyer There are some fixed buyers of the industry. The buyers give their orders continuously all over the year. The

marketing officers & by both side understanding The rate & the order quantity are fixed.

Duties & Responsibilities Of Marketing Officer:

Dealing with the buyer & convince the buyer is the main duty of the marketing officer. A marketing officer has some also other duties The main duties & responsibilities of a marketing officer are given below :

•	To prepare cost sheet by dealing with buyer .

•	To take different steps by discussing with the high officials & merchandisers .

•	To maintain a regular & good relationship between commercial officers & merchandisers .

•	To maintain a regular communication with the buyers & buying houses .

•	Communicate with the new buyers .

•	Display the better criteria of the products .

•	Actually the responsibilities & duties of marketing officer begins from getting order of   buyer & ends after        receiving goods by the buyer So he should be always smart energetic & sincere.

REMARKS:

FNL has a well learned marketing & merchandising team. They always communicate with

the buyers FNL has some fixed buyers The marketing section also looks for the quality & quantity of buyers .

We have completed our industrial attachment successfully by the grace of Almighty.

Industrial attachment sends us to the expected destiny of practical life The completion of the two months Industrial Attachment at FARIHA KNIT TEX LTD., we have got the impression that the factory is one of the most modern export oriented knit composite in Bangladesh Though it was established only a few year's ago ,it has earned " very good reputations "

For its best performance over many other export oriented textile mills .

Mill is settled with utility to give all convenient supports to the productions for twenty-four hours . FNLhas its own water pre-treatment plant & 26,300 cubic feet water reservoirs in its Godnail campus The Godnail premises has its own power generation plant where 1,900 kw power generators guarantee smooth & uninterrupted power supply to its every operation .

However there are some points to be mentioned :

•	During the transport of the fabric in the dyeing floor & also during the loading of the machine, fabrics are soiled for the contact with floor. This makes the fabric/part of the fabric dirty. It may require more scouring/bleaching agent or may create stain making it faulty.

The- dyeing floor is watery most of the time. It should be cleaned all	the time.

•	Many time the dosing pipelines are clogged due to the careless dosing of the chemicals. The supervisors should supervise the floor more sincerely.

•	The machine stoppage time should be analyzed & minimized. The maintenance should be carried out when the machine is out of action (wherever possible).

OUR APOLOGY :

•	The management of FNL are very helpful Our respective seniors gave us time when ever they got .

•	Due to secrecy act, all the data on costing & marketing activities has not been supplied & hence this report excludes these chapters.

•	Some of the points in different chapter are not described as these were not available.

•	The whole process is not possible to bind in such a small frame as this report, hence our effort spent on summarizing them.

•	But it must be said that FNL is a best place to get the practical knowledge about the dyeing as they have lot of production of all quality .

We are enough fortunate that we have got an opportunity of having a training in this mill During the training period we are received co-operation & association from the authority full & found all man , machines & materials on appreciable working condition All stuffs & officers are very sincere & devoted there duties to achieve their goal.

# Text boxes

LOCATION OF FNL

FATULLAH BISIC

Room Temperature

60▫C × 5'

98▫C × 60'

2▫C /min

80▫C

H2O2

1     2     3     4     5      6     7

1) Anticreasing

2) Wetting Agent

3) sequestering Agent

4) Antifoam

5) stabilizer

6) Soda

7) Caustic

Cold Wash

5'

5'

Cold Wash

Room Temperature

60▫C × 5'

80▫C × 15'

1                   2

1) Oxalic Acid

2) Peroxide Killer

Cold Wash

Cold Wash

5'

5'

PH= 4.5-5

55▫C × 60'

70▫C × 10'

1                   2

1) Acetic Acid

2) Bio-Polish

Cold Wash

Cold Wash

5'

5'

Room temperature

60▫C × 60'

1        2         3          4

1) Auxilaries

2) Salt

3) Color dosing(20-30')

4)Soda dosing(30-40')

Cold Wash

Cold Wash

5'

5'

Cold Wash

5'

60▫C × 10'

Acetic acid

20'

60▫C

90▫C

80▫C

80▫C

Soaping chemical

50▫C × 20′

Fixing agent    Softner

20′

40▫C × 20′

Softener &

Acid

35▫C × 10'

50▫C × 60'

1   2    3    4       5

1) Auxilaries

2) Dyes

3) Gluber salt

4)Fabric

5)Soda ash

35▫C × 5'